## Slide 1: Harvard System-Theory Talk Series
Minlan Yu
Harvard University
Algorithms in Programmable Switches

## Slide 2: Exciting Times in Systems
Machine learning
Video Analytics
Cloud
Streaming games
Cloud assisted Self-driving cars
Increasing needs for high throughput and low latency

## Slide 3: Compute Cannot Keep Up with Data Growth
Significant data growth
  The data created and consumed worldwide to exceed 180 Zetabytes by 2025
Compute cannot keep up
  Facing the end of Moore’s law

## Slide 4: The Rise of Heterogeneous Devices
Compute:
GPU, TPU, FPGA
Network:
Programmable switches
Smart NICs
RDMA
Storage:
Non-volatile memory
SSDs
Provide high throughput and low latency for specific functions

## Slide 5: Fundamental Challenge 1
How to provide high performance for applications
by leveraging the full potential of heterogeneous devices?

## Slide 6: Increasing Network Scale
Cloud:
Hundreds of thousands of switches
Millions of servers
Edge:
Billions of IoT devices

## Slide 7: Fundamental Challenge 2
Measure:
Detailed, real-time,
large-scale telemetry data
Control:
Fast, automated, programmable decisions
  Self-driving networks
  How to manage many heterogeneous devices with a fast measure-control loop?

## Slide 8: Call for Theoretical Contributions
How to provide high performance for applications by leveraging the full potential of heterogeneous devices?
  Compact data structures, streaming algorithms
  Given the programmability, memory, and network constraints
  Resource allocation across applications
How to manage many heterogeneous devices with a fast measure-control loop?
  Distributed algorithms for coordination
  Approximation algorithms
  Division of labor across many parties

## Slide 9: Example: Programmable Switches
+ High throughput: Multi-Tbps
+ Low Latency: <1us per packet

## Slide 10: Two Example Applications on Programmable Switches
Network telemetry
  Collect fine-grained data across many switches while supporting diverse queries?
  High throughput, low latency for self-driving networks
In-network computing
  Offload high-level applications to switches
  Database queries: Low query completion time
  DDoS defenses: High throughput

## Slide 11: Challenges of Programmable Switches
Significant data growth
Limited memory
Diverse programs
Limited programmability
Increasing line rate
Limited per packet processing
Growing applications
Switch limitations

## Slide 12: Two Example Applications on Programmable Switches
Network telemetry
  Collect fine-grained data across many switches while supporting diverse queries?
  In-network telemetry: Reduce bits in packets
  Direct-telemetry access: Reduce collection overhead
In-network computing
  Offload high-level applications to switches for high throughput
  Database queries: Run best effort queries at switches
  DDoS defense: Support diverse defense tasks with limited resources.

## Slide 13: Network Telemetry

## Slide 14: Network Telemetry
14
  … …
  … …
  … …
Network queries on the collector
Attack detection
Perf. Diagnosis
Traffic engineering

## Slide 15: Measuring Packet-level Events
Diverse queries on packet lifetime
  Which path do my packets take?
  Which firewall rules do my packets follow?
  Which switch/link has the highest latency for my packets?
Useful for real-time control and feedback loop
  E.g., congestion control, load balancing, troubleshooting, etc.

## Slide 16: INT: In-band Network Telemetry
pkt
pkt
pkt
INT
INT
Sender
Receiver
INT: add switch states in packets and analyze at the receiver
  E.g., Switch ID, Queuing delay, link utilization
Already supported in switches today
Notes: Brings insight into packet lifetime, already supported in

## Slide 17: Key Problems
High bit overhead
  Path query w/ a single telemetry info (switch ID): 28 Bytes
  Even more bytes if we add other info (e.g., queuing delay, timestamps)
  Lead to up to 20% goodput drop
High processing overhead
  Collect such information from many switches to a centralized collector
  High bandwidth and processing overhead at the collector

## Slide 18: Reduce Bit Overhead
PINT: Probabilistic In-band Network Telemetry
  Encode telemetry information on packets with fewer bits
Insight
  Most apps don’t need per-packet per-switch values, but aggregated data
  Leverage probabilistic solutions to aggregate across packets and flows

## Slide 19: Data Aggregation in PINT
Static Per-flow aggregation
  For a flow with packets 𝑝_1,𝑝_2,…
  E.g., flow-level path tracing
Packets
Switches
Output
Static Per-flow

## Slide 20: Data Aggregation in PINT
dynamic per flow aggregation
  For each switch on the path, aggregate (e.g., estimate the median) over 𝑣(𝑝_1,𝑠),𝑣(𝑝_2,𝑠),….
  E.g., median/tail latency of (switch, flow) pairs
20
Packets
Switches
Dynamic Per-flow

## Slide 21: Flow-level Path Tracing
Coordination with explicit messages
  Put one switch ID in each packet
  Global hash function based on packet and hop ID
  Run Reservoir Sampling (Sattari et al., 2010) for uniform sampling
A Coupon Collector process.
  For hops it will take packets to detect the path.
A
B
C
D
C
A
A
D
A
C
B
Notes: Coordinate switches without explicit collaboration
run Reservoir Sampling (Sattari et al., 2010).

## Slide 22: Coupon Collector Process
Number of samples
22

## Slide 23: The Power of Coding
A
B
Baseline:
Get information on the first packet.
Require 2 packets on average to get the second hop ID.
  Overall: packets in expectation.
Coding solution:
Consider baseline sampling with probability 0.5, and writing otherwise.
If the first packet is an ID (e.g., ), we need more packets on average.
If the first packet is , we need 2 more packets
  Overall: packets in expectation.
𝐴⊕𝐵
Notes: In contrast, consider an algorithm that uses this sampling with probability 50%, and otherwise writes the bitwise-xor of both IDs. That is, each packet has probability 25% to carry the ID $A$, 25% to have $B$, and 50% to have $A\oplus B$. This modification reduces the expected number of packets we require to $8/3$. For example, if the first packet carried $A$, we have a probability of 75% of inferring $B$ in each consecutive packets. This is because we get B itself w.p. 25%, and A$\oplus$B with 50%. When getting $A\oplus B$, we can get $B$ from $A\oplus(A\oplus B)$ since we already know A.

## Slide 24: Improve the Coupon Collector w/ XOR Coding
24
Number of samples
Baseline
XOR
XOR

## Slide 25: Complete Algorithm
Coupon collector
XOR1
XOR2
  With probability , run the coupon collector algorithm.
  Otherwise, choose one XOR layer at random.
  The XOR instances have increasing probabilities.
Notes: Comparison with Linear Network Coding. Several algorithms can be adapted to work in the distributed encoding setting. For example, Linear Network Coding (LNC) [32] allows one to decode a message in a near-optimal number of packets by taking random linear combinations over the message blocks. That is, on every packet, each block is xor-ed into its digest with probability 1/2. Using global hash functions to select which blocks to xor, one can determine the blocks that were xor-ed onto each digest. LNC requires just ≈ k + log2 k packets to decode the message. However, in some cases, LNC may be suboptimal and PINT can use alternative solutions. First, the LNC decoding algorithm requires matrix inversion which generally takes O(k 3 ) time in practice (although theoretically faster algorithms are possible). If the number of blocks is large, we may opt for approaches with faster decoding. Second, LNC does not seem to work when using hashing to reduce the overhead. As a result, in such a setting, LNC could use fragmentation, but may require a larger number of packets than the XOR-based scheme using hashing.

## Slide 26: Key Problems
High bit overhead
  Global hash function and reservoir sampling
  Randomized algorithm with XOR-based encoding
High processing overhead
  Collect such information from many switches to a centralized collector
  High bandwidth and processing overhead at the collector

## Slide 27: Aggregating Network Data to a Collector
Telemetry generates tons of data!
  Overloads collector CPU
  Reduced insight
We redesign telemetry collection
  Bypassing the CPU
  Increased insight
Reports
RDMA
O(1Mpps)
Per switch & metric
Introduce RDMA here
“we use RDMA with is HPC tech to bypass CPU” “okay to repeat some”
Add spoken: “of course I’m gonna show it’s not as simple as just ‘use RDMa and it works’”
Take it already here
End “but why do we need to redesign it?”
Notes: [End] But why is this a problem now? What has changed?

## Slide 28: But RDMA is limited...
[2]=c
[2]=e
0
1
2
3
a
a
b
_
_
c
Limited verbs
  Read, Write, Fetch-and-Add, Compare-and-Swap
  Cannot support complex data structures
Limited # of RDMA connections
  Need queues and states per connection
  Cannot scale to many switches
Assume lossless network

## Slide 29: Direct Telemetry Access with A Translator
RDMA
Collector
Translator (ToR)
DTA
Limited verbs
  Switch-level primitive extensions
Limited # of RDMA connections
  Translator aggregates connections across switches
Assume lossless network
  Flow control between switches and translator
Notes: Potential question: “But you still use RDMA!!!”
Explain some benefits of just a single RDMA link

## Slide 30: Key-Write
For key-value store
  E.g., (5 tuple flows, counters)
A shared hash table across switches
  With global hash function on arbitrary keys
  Problem: Collisions, data overwrite
N redundant data insertions
  Checksum to validate keys
  Plurality vote on values
Provable bounds on missing or wrong values
Fig: Data indexing, N=3

## Slide 31: Postcard Write
Each switch sends postcards to the collector
  E.g., tracing a flow path: (packet/flow ID, switch hop, Data)
Strawman: Key-Write
  Many random memory accesses
Postcard Write: aggregate hops for the same flow into chunks
  Assume each path has at most B hops
  Translator batches writes to improve performance and reduce collisions
  Allow N redundancy writes
  4.3x faster than Key-Write

## Slide 32: Postcards with Encoding
Strawman solution:
  Write value and checksum directly in each slot
Instead, encoding to reduce bits
  Hashing value to fixed #bits
  XOR checksum of key with hashed value
  Can still extract values by enumerating hops

## Slide 33: Key Problems and Solutions
PINT: Reduce bit overhead
  Global hash function and reservoir sampling
  Randomized algorithm with XOR-based encoding
DTA: reduce collector overhead
  Introduce a translator to support new primitives for complex data structures
  Global hash table with redundant insertion
  Batching and encoding for postcards across hops

## Slide 34: Theoretical Questions in Network Telemetry
Reduce bits in packets and memory
  Hashing, encoding, approximation
  By leveraging redundances across hops, packets, and flows
Coordinate with minimal messages
  Answer a network-wide query with switch-local information
  Coordinate across switches, hosts, and collectors
Support diverse queries
  Query-based optimization of data structures given limited programmability
  Resource sharing across queries
How to redesign systems to make theory easier
Notes: Given limited programmability at switches and RDMA

## Slide 35: In-Network Computing

## Slide 36: Distributed Data Processing Applications
databases
Key-value stores
ML training & inferences
DDoS Defenses
Can programmable switches help improve the performance?
Switches already sit in the network;
provide high throughput and low latency for some functions
Increasing needs for high throughput and low latency
Notes: Distributed data processing applications are the critical infrastructure for many applications and services.
Banking, education, social networks, online shopping, and manufacturing

## Slide 37: Two examples
Offload database queries
  Complex queries
  Limited programmability and resources at switches
  Best effort at switches
Offload DDoS detection
  Diverse detection and mitigation modules
  Limited resources at switches
  Full defenses at switches

## Slide 38: Cheetah: Accelerate Database Queries via Switches
Database queries
  Multiple workers parallelize data processing
  A master node aggregate results and answer the query
Use switches to accelerate the data processing
Worker
Data
User
Query
Query planner
Master Node
Plan
Switch
Query
Result
Data

## Slide 39: Key Challenges of Using Programmable Switches
Memory
0 | 
1 | 
2 | 
3 | 
0 | 
1 | 
2 | 
3 | 
0 | 
1 | 
2 | 
3 | 
39
Limitation 1:
small number of stages
Limitation 2:
small per-stage memory
Limitation 3:
Supports basic arithmetic ops

## Slide 40: The Pruning Abstraction
Query on pruned dataset = Query on original dataset
Worker
Master Node
Switch
A, B, A, A, C, D, D, E, A, B, C, C, D, A, E, A, D, A, C
A, B, A, C, D, E, B, A, E, A, A, C
A, B, C, D, E
Pruned data set using switches
Original dataset
Query results

## Slide 41: Example: Distinct Query Pruning
Selects all the distinct values
  SELECT DISTINCT seller FROM Products
Strawman solution: Bloom Filters
  Problem: False positives which may drop distinct entries
A, B, A, A, C, D, D, E, A, B, C, C, D, A, E, A, D, A, C
A, B, A, C, D, E, B, A, E, A, A, C
A, B, C, D, E
Pruned data set using switches
Original dataset
Query results
Notes: Is this deployed anywher?

## Slide 42: Example: Distinct Query Pruning
Selects all the distinct values
  SELECT DISTINCT seller FROM Products
Strawman solution: Bloom Filters
  Problem: False positives which may drop distinct entries
But a cache works!
  Implement LRU with a rolling replacement across stages
Our solution: Multi-row LRU cache
  Hash packets to a row
  Reduce #per-packet comparison
Notes: Is this deployed anywher?

## Slide 43: Cheetah Results
Many Queries
  Distinct, Top N
  Join, Group-By, Having
  Skyline, Filtering
  and their combinations
Spark + Tofino implementation
  github.com/harvard-cns/cheetah-release
  40-75 % faster completion time on database benchmarks
E.g., TPC-H Query 3

## Slide 44: Two examples
Offload database queries
  Complex queries
  Limited programmability and resources at switches
  Best effort at switches
Offload DDoS detection
  Diverse detection and mitigation modules
  Limited resources at switches
  Broad-spectrum defenses at switches

## Slide 45
Jaqen: Switch-Native DDoS Defense for ISP
DDoS
Victims
Provide large volumes with low latency
Handle diverse attack vectors for both detection and mitigation
ISP network as a defender
Notes: To answer this question, our vision is a switch-native ddos defense system called Jaqen that turns an ISP network into a defender. No out-of-band detection, no scrubbing centers, no what’s so ever.
Jaqen integrates detection and mitigation completely in the programmable switches and designed for switch-native mitigation efforts towards volumetric attacks.

## Slide 46
Jaqen’s Full Stack Design
DDoS
Victims
1.
Broad-Spectrum Detection
2.
3.
Controller
Dynamic Resource Allocation
Fast On-demand Mitigation
Notes: In jaqen, we have three compoents

## Slide 47
Broad-Spectrum and Always-On Detection
Packet
Parser
…
+
+
+
+
+
Universal Sketches
Attack Signatures
SYN
RST
DNS
NTP
…
…
Attack types
Attack volumes
Unidentified
A wide-spectrum detection of volumetric attacks.
Compact design with future-proof universal sketches.
Detection metric API: Query (proto, func, mode, freq)
e.g., elephant flows, distinct flows, heavy sources, entropy
Notes: In the Detection components, our design leverage universal sketches to estimate a large range of statistics or even unforeseen functions for different flow identities.
In addition to the sketches, we add a few signature counters as a complement
Together, we can estimate various attacks and volumes.
For users, we provide
Mode: pulling or pushing
To that end, we design an API with Query(proto,func,mode ,freq) to precisely obtain the metrics for detection, where proto defines the queried protocol, func defines the function of the metric, mode defines the reporting mode (e.g., self-triggering with a threshold), and freq is the reporting frequency. For example, we can query the UDP srcIP heavy flows above a 0.5% threshold every 5 seconds in a self-reporting mode. A

## Slide 48
Fast On-Demand Mitigation
Detection results
Available resources
Quick resource allocation
(Optimization solver)
Mitigation Modules:
M1, M2, M3, …
Cannot afford preloading all possible mitigation modules.
Notes: Once we have the detection results, along with the network-wide available resources

## Slide 49
Switch-Optimized Mitigation Library
Best-practice mitigation
SYN Cookie/proxy [BSDC’02, RFC4987]
Block-List [WDFIA’07]
Allow-List [WDFIA’07]
ICMP block
DNS filter
…
Switch-optimized library
Sketches
Bloom filters
Counting bloom filters
SYN Proxy with filters
Exact-match table
Rater limiter
…
Preserve O(10 Million) legitimate connections
with O(10 MB) on-switch memory.
Support mitigation strategies on 21 attacks.
Mitigation API
Notes: In designing mitigation modules, we explore a set of best-practice mitigation strategies, extract their workflow as a few key components and redesign each component with efficient probabilistic data structures. Finally, we provide API for each component to help construct mitigation strategies for current and possibly future attacks.

## Slide 50
Switch-Native SYN Proxy
Client
SYN Proxy
Server
SYN
SYN-ACK
w/ cookie
ACK w/ cookie+1
SYN-ACK
SYN
ACK
SYN Cookie & conn table
Verify cookie
Client
Switch
Server
SYN
Error SYN-ACK
w/ cookie
RST
w/ cookie
SYN-ACK
SYN
ACK
Cookie w/o states
Verify cookie +allowlist
SYN Proxy [NDSS’20]
Jaqen SYN Proxy
Seq. # adjustment
Per-conn state!
Bloom filter for the allowlist
Notes: Generate RST with received seq number
Implementing mitigation functions in switches require careful redesign.
Only keep those data that have passed the test. Bloom filter
The typical workflow of a SYN proxy can be described as: (1) When a SYN is received, the proxy server generates a unique cookie [69] with 5-tuple and adds it to the sequence number (seq. no.) header field of the corresponding SYN-ACK reply. (2) When a legitimate client receives the SYN-ACK it will acknowledge back an ACK packet with cookie+1 in its seq. no.; Otherwise, an attacker would not send the cookie back. (3) Once the proxy verifies the correctness of the cookie, it will record session information (e.g., seq. no. difference) and construct a new SYN to the designated destination to establish the connection. The succeeding packets will go through the proxy to translate the seq. no. in order to continue the original TCP handshake.
Unfortunately, the current switch-based SYN proxy that directly implements the above server-based design (e.g., Poseidon [3]) has scalability issues when there is a large number of legitimate connections. They maintain seq. no. translation data for each legitimate connection using a single hash table (e.g., size 65536). Inevitably, using a single hash table for per-connection state storage would break the correctness of many legitimate connections due to hash collisions. For instance, keeping 65536 legitimate connections on a hash table of size 65536 has expected 24109 collisions.4 To address this issue, we design two SYN proxy modes with HeaderHashAndTest(identity,action) to perform a “cookie” operation on designated header fields with hashing and send back a response packet (e.g., SYN-ACK) to “test” if the client is legitimate. Note that in our design, one can use ApproxAllowList(identity,config) to record a large number of legitimate identities that have passed the tests. The approximation errors will not affect legitimate traffic since Bloom filters do not create false negatives.

## Slide 51: Two examples
Offload database queries
  Complex queries
  Limited programmability and resources at switches
  Best effort at switches
Offload DDoS detection
  Diverse detection and mitigation modules
  Limited resources at switches
  Broad-spectrum defenses at switches

## Slide 52: Theoretical Questions for In-Network Computing
Complex functions vs limited programmability
  Redesign algorithms with new constraints
Division of labor
  Best effort at switches; Full query at hosts
  Broad-spectrum detection vs on demand mitigation
Room for approximation
  Compensate with host functions and system design
  Understand system impact of different approximation solutions

## Slide 53: Going Forward…
Systems
  Programmable switches
  Smart NICs
  FPGA
  Storage, Compute
  Edge servers, IoTs
  A broader set of applications
Theory
  Hashing, coding, randomization
  Distributed algorithms
  Queuing
  Scheduling
  Caching
  Machine learning

## Slide 54: Going Forward…
A theoretical foundation for systems
  Programmable switches as an example:
  Formal models on switch capabilities and resource tradeoffs
  A library of data structures and algorithms for switches
Redesign systems to facilitate theory design
  Programmable switches as an example:
  What new features should we add to systems?
  How to realize theoretical assumptions in practice?

## Slide 55: Thank you!